## Slide 1
PowerPoint presentation to accompany
Heizer, Render, Munson
Operations Management, Twelfth Edition, Global Edition
Principles of Operations Management, Tenth Edition, Global Edition
PowerPoint slides by Jeff Heyl
Short-Term Scheduling
15

## Slide 2: Learning Objectives
When you complete this chapter you should be able to:
15.1 Explain the relationship between short-term scheduling, capacity planning, aggregate planning, and a master schedule
15.2 Apply the assignment method for loading jobs
15.3 Name and describe each of the priority sequencing rules
15.4 Use Johnson’s rule
15.5 Use the cyclical scheduling technique

## Slide 3: Short-Term Scheduling
The objective of scheduling is to allocate and prioritize demand (generated by either forecasts or customer orders) to available facilities

## Slide 4: Importance of Short-Term Scheduling
Effective and efficient scheduling can be a competitive advantage
  Faster movement of goods through a facility means better use of assets and lower costs
  Additional capacity resulting from faster throughput improves customer service through faster delivery
  Good schedules result in more dependable deliveries

## Slide 5: Scheduling Issues
Scheduling deals with the timing of operations
The task is the allocation and prioritization of demand
Significant factors are
  Forward or backward scheduling
  Finite or infinite loading
  The criteria for sequencing jobs

## Slide 6: Scheduling Flow
Figure 15.1

## Slide 7: Forward and Backward Scheduling
Forward scheduling starts as soon as the requirements are known
Produces a feasible schedule though it may not meet due dates
Frequently results in buildup of work-in- process inventory
Due Date
Now

## Slide 8: Forward and Backward Scheduling
Backward scheduling begins with the due date and schedules the final operation first
Schedule is produced by working backwards though the processes
Resources may not be available to accomplish the schedule
Due Date
Now

## Slide 9: Forward and Backward Scheduling
Backward scheduling begins with the due date and schedules the final operation first
Schedule is produced by working backwards though the processes
Resources may not be available to accomplish the schedule
Due Date
Now
Often these approaches are combined to develop a trade-off between capacity constraints and customer expectations

## Slide 10: Finite and Infinite Loading
Assigning jobs to work stations
Finite loading assigns work up to the capacity of the work station
  All work gets done
  Due dates may be pushed out
Infinite loading does not consider capacity
  All due dates are met
  Capacities may have to be adjusted

## Slide 11: Assignment Method
A special class of linear programming models that assigns tasks or jobs to resources
Objective is usually to minimize cost or time
Only one job (or worker) is assigned to one machine (or project)

## Slide 12: Assignment Method
Build a table of costs or time associated with particular assignments
 | TYPESETTER |  | 
JOB | A | B | C
R-34 | $11 | $14 | $ 6
S-66 | $ 8 | $10 | $11
T-50 | $ 9 | $12 | $ 7

## Slide 13: Assignment Method
Create zero opportunity costs by repeatedly subtracting the lowest costs from each row and column
Draw the minimum number of vertical and horizontal lines necessary to cover all the zeros in the table. If the number of lines equals either the number of rows or the number of columns, proceed to step 4. Otherwise proceed to step 3.

## Slide 14: Assignment Method
Subtract the smallest number not covered by a line from all other uncovered numbers. Add the same number to any number at the intersection of two lines. Return to step 2.
Optimal assignments are at zero locations in the table. Select one, draw lines through the row and column involved, and continue to the next assignment.

## Slide 15: Assignment Example
A B C
Job
R-34 $11 $14 $ 6
S-66 $ 8 $10 $11
T-50 $ 9 $12 $ 7
Typesetter
A B C
Job
R-34 $ 5 $ 8 $ 0
S-66 $ 0 $ 2 $ 3
T-50 $ 2 $ 5 $ 0
Typesetter
Step 1a - Rows
A B C
Job
R-34 $ 5 $ 6 $ 0
S-66 $ 0 $ 0 $ 3
T-50 $ 2 $ 3 $ 0
Typesetter
Step 1b - Columns

## Slide 16: Assignment Example
Step 2 - Lines
A B C
Job
R-34 $ 5 $ 6 $ 0
S-66 $ 0 $ 0 $ 3
T-50 $ 2 $ 3 $ 0
Typesetter
Because only two lines are needed to cover all the zeros, the solution is not optimal
A B C
Job
R-34 $ 3 $ 4 $ 0
S-66 $ 0 $ 0 $ 5
T-50 $ 0 $ 1 $ 0
Typesetter
Step 3 - Subtraction
The smallest uncovered number is 2 so this is subtracted from all other uncovered numbers and added to numbers at the intersection of lines
Smallest uncovered number

## Slide 17: Assignment Example
Because three lines are needed, the solution is optimal and assignments can be made
Step 2 - Lines
A B C
Job
R-34 $ 3 $ 4 $ 0
S-66 $ 0 $ 0 $ 5
T-50 $ 0 $ 1 $ 0
Typesetter
Start by assigning R-34 to worker C as this is the only possible assignment for worker C.
Step 4 - Assignments
A B C
Job
R-34 $ 3 $ 4 $ 0
S-66 $ 0 $ 0 $ 5
T-50 $ 0 $ 1 $ 0
Typesetter
Job T-50 must go to worker A as worker C is already assigned. This leaves S-66 for worker B.

## Slide 18: Assignment Example
From the original cost table
Minimum cost = $6 + $10 + $9 = $25
A B C
Job
R-34 $11 $14 $ 6
S-66 $ 8 $10 $11
T-50 $ 9 $12 $ 7
Typesetter
A B C
Job
R-34 $ 3 $ 4 $ 0
S-66 $ 0 $ 0 $ 5
T-50 $ 0 $ 1 $ 0
Typesetter

## Slide 19
Machine Assignment Example
1. Determine the job assignment to the machine which maximizes total production!
2. What is the total assignment production?
Job | Machine |  |  | 
 | A | B | C | D
1 | 7 | 9 | 8 | 10
2 | 10 | 9 | 7 | 6
3 | 11 | 5 | 9 | 6
4 | 9 | 11 | 5 | 8

## Slide 20
Solution:
Job | Machine |  |  | 
 | A | B | C | D
1 | 7 | 9 | 8 | 10
2 | 10 | 9 | 7 | 6
3 | 11 | 5 | 9 | 6
4 | 9 | 11 | 5 | 8
Job | Machine |  |  | 
 | A | B | C | D
1 | 3 | 1 | 2 | 0
2 | 0 | 1 | 3 | 4
3 | 0 | 6 | 2 | 5
4 | 2 | 0 | 6 | 3

## Slide 21
Solution:
Job | Machine |  |  | 
 | A | B | C | D
1 | 3 | 1 | 0 | 0
2 | 0 | 1 | 1 | 4
3 | 0 | 6 | 0 | 5
4 | 2 | 0 | 4 | 3
Job | Machine |  |  | 
 | A | B | C | D
1 | 3 | 1 | 0 | 0
2 | 0 | 1 | 1 | 4
3 | 0 | 6 | 0 | 5
4 | 2 | 0 | 4 | 3

## Slide 22
assignment Schedul :
1 D = 10
2 A = 10
3 C = 9
4 B = 11
---------------------------------
Total Production = 40

## Slide 23: Sequencing Jobs
Specifies the order in which jobs should be performed at work centers
Priority rules are used to dispatch or sequence jobs
  FCFS: First come, first served
  SPT: Shortest processing time
  EDD: Earliest due date
  LPT: Longest processing time

## Slide 24: Performance Criteria
Flow time – the time between the release of a job to a work center until the job is finished
Average completion time =
Sum of total flow time
Number of jobs
Utilization metric =
Total job work (processing) time
Sum of total flow time
Average number of
jobs in the system
=
Sum of total flow time
Total job work (processing) time
Average job lateness =
Total late days
Number of jobs

## Slide 25: Performance Criteria
Flow time – the time between the release of a job to a work center until the job is finished
Average completion time =
Sum of total flow time
Number of jobs
Utilization metric =
Total job work (processing) time
Sum of total flow time
Average number of
jobs in the system
=
Sum of total flow time
Total job work (processing) time
Average job lateness =
Total late days
Number of jobs
Job lateness = Max{0, yesterday + flow time – due date}

## Slide 26: Sequencing Example
Job | Job Work (Processing) Time (Days) | Job Due Date (Days)
A | 6 | 8
B | 2 | 6
C | 8 | 18
D | 3 | 15
E | 9 | 23
Apply the four popular sequencing rules to these five jobs

## Slide 27: Sequencing Example
Job Sequence | Job Work (Processing) Time |  |  | Flow Time |  |  | Job Due Date | Job Lateness |  | 
A |  | 6 |  |  | 6 |  | 8 |  | 0 | 
B |  | 2 |  |  | 8 |  | 6 |  | 2 | 
C |  | 8 |  |  | 16 |  | 18 |  | 0 | 
D |  | 3 |  |  | 19 |  | 15 |  | 4 | 
E |  | 9 |  |  | 28 |  | 23 |  | 5 | 
 |  | 28 |  |  | 77 |  |  |  | 11 | 
FCFS: Sequence A-B-C-D-E

## Slide 28: Sequencing Example
FCFS: Sequence A-B-C-D-E
Average completion time = = 77/5 = 15.4 days
Sum of total flow time
Number of jobs
Utilization metric = = 28/77 = 36.4%
Total job work (processing) time
Sum of total flow time
Average number of jobs in the system
= = 77/28 = 2.75 jobs
Sum of total flow time
Total job work time
Average job lateness = = 11/5 = 2.2 days
Total late days
Number of jobs

## Slide 29: Sequencing Example
SPT: Sequence B-D-A-C-E
Job Sequence | Job Work (Processing) Time |  |  | Flow Time |  |  | Job Due Date | Job Lateness |  | 
B |  | 2 |  |  | 2 |  | 6 |  | 0 | 
D |  | 3 |  |  | 5 |  | 15 |  | 0 | 
A |  | 6 |  |  | 11 |  | 8 |  | 3 | 
C |  | 8 |  |  | 19 |  | 18 |  | 1 | 
E |  | 9 |  |  | 28 |  | 23 |  | 5 | 
 |  | 28 |  |  | 65 |  |  |  | 9 | 

## Slide 30: Sequencing Example
SPT: Sequence B-D-A-C-E
Average completion time = = 65/5 = 13 days
Sum of total flow time
Number of jobs
Utilization metric = = 28/65 = 43.1%
Total job work time
Sum of total flow time
Average number of jobs in the system
= = 65/28 = 2.32 jobs
Sum of total flow time
Total job work time
Average job lateness = = 9/5 = 1.8 days
Total late days
Number of jobs

## Slide 31: Sequencing Example
Job Sequence | Job Work (Processing) Time |  |  | Flow Time |  |  | Job Due Date | Job Lateness |  | 
B |  | 2 |  |  | 2 |  | 6 |  | 0 | 
A |  | 6 |  |  | 8 |  | 8 |  | 0 | 
D |  | 3 |  |  | 11 |  | 15 |  | 0 | 
C |  | 8 |  |  | 19 |  | 18 |  | 1 | 
E |  | 9 |  |  | 28 |  | 23 |  | 5 | 
 |  | 28 |  |  | 68 |  |  |  | 6 | 
EDD: Sequence B-A-D-C-E

## Slide 32: Sequencing Example
EDD: Sequence B-A-D-C-E
Average completion time = = 68/5 = 13.6 days
Sum of total flow time
Number of jobs
Utilization metric = = 28/68 = 41.2%
Total job work time
Sum of total flow time
Average number of jobs in the system
= = 68/28 = 2.43 jobs
Sum of total flow time
Total job work time
Average job lateness = = 6/5 = 1.2 days
Total late days
Number of jobs

## Slide 33: Sequencing Example
Job Sequence | Job Work (Processing) Time |  |  | Flow Time |  |  | Job Due Date | Job Lateness |  | 
E |  | 9 |  |  | 9 |  | 23 |  | 0 | 
C |  | 8 |  |  | 17 |  | 18 |  | 0 | 
A |  | 6 |  |  | 23 |  | 8 |  | 15 | 
D |  | 3 |  |  | 26 |  | 15 |  | 11 | 
B |  | 2 |  |  | 28 |  | 6 |  | 22 | 
 |  | 28 |  |  | 103 |  |  |  | 48 | 
LPT: Sequence E-C-A-D-B

## Slide 34: Sequencing Example
LPT: Sequence E-C-A-D-B
Average completion time = = 103/5 = 20.6 days
Sum of total flow time
Number of jobs
Utilization metric = = 28/103 = 27.2%
Total job work time
Sum of total flow time
Average number of jobs in the system
= = 103/28 = 3.68 jobs
Sum of total flow time
Total job work time
Average job lateness = = 48/5 = 9.6 days
Total late days
Number of jobs

## Slide 35: Sequencing Example
Rule | Average Completion Time (Days) | Utilization Metric (%) | Average Number of Jobs in System | Average Lateness (Days)
FCFS | 15.4 | 36.4 | 2.75 | 2.2
SPT | 13.0 | 43.1 | 2.32 | 1.8
EDD | 13.6 | 41.2 | 2.43 | 1.2
LPT | 20.6 | 27.2 | 3.68 | 9.6
Summary of Rules

## Slide 36: Comparison of Sequencing Rules
No one sequencing rule excels on all criteria
SPT does well on minimizing flow time and number of jobs in the system
  But SPT moves long jobs to the end which may result in dissatisfied customers
FCFS does not do especially well (or poorly) on any criteria but is perceived as fair by customers
EDD minimizes maximum lateness

## Slide 37: Critical Ratio (CR)
An index number found by dividing the time remaining until the due date by the work time remaining on the job
Jobs with low critical ratios are scheduled ahead of jobs with higher critical ratios
Performs well on average job lateness criteria
CR = =
Due date – Today's date
Work (lead) time remaining
Time remaining
Workdays remaining

## Slide 38: Critical Ratio Example
JOB | DUE DATE | WORKDAYS REMAINING
A | 30 | 4
B | 28 | 5
C | 27 | 2
Currently Day 25
With CR < 1, Job B is late. Job C is just on schedule and Job A has some slack time.
JOB | CRITICAL RATIO | PRIORITY ORDER
A | (30 - 25)/4 = 1.25 | 3
B | (28 - 25)/5 = .60 | 1
C | (27 - 25)/2 = 1.00 | 2

## Slide 39: Critical Ratio Technique
Determine the status of a specific job
Establish relative priorities among jobs on a common basis
Adjust priorities automatically for changes in both demand and job progress
Dynamically track job progress

## Slide 40: Sequencing N Jobs on Two Machines: Johnson's Rule
Works with two or more jobs that pass through the same two machines or work centers
Minimizes total production time and idle time
An N/2 problem, N number of jobs through 2 workstations

## Slide 41: Johnson’s Rule
List all jobs and times for each work center
Select the job with the shortest activity time. If that time is in the first work center, schedule the job first. If it is in the second work center, schedule the job last. Break ties arbitrarily.
Once a job is scheduled, it is eliminated from the list
Repeat steps 2 and 3 working toward the center of the sequence

## Slide 42: Johnson’s Rule Example
JOB | WORK CENTER 1 (DRILL PRESS) | WORK CENTER 2 (LATHE)
A | 5 | 2
B | 3 | 6
C | 8 | 4
D | 10 | 7
E | 7 | 12

## Slide 43: Johnson’s Rule Example
A
C
B
D
E
JOB | WORK CENTER 1 (DRILL PRESS) | WORK CENTER 2 (LATHE)
A | 5 | 2
B | 3 | 6
C | 8 | 4
D | 10 | 7
E | 7 | 12

## Slide 44: Johnson’s Rule Example
Time 0 3 10 20 28 33
B
A
C
D
E
WC 1
WC 2
B
A
C
D
E
JOB | WORK CENTER 1 (DRILL PRESS) | WORK CENTER 2 (LATHE)
A | 5 | 2
B | 3 | 6
C | 8 | 4
D | 10 | 7
E | 7 | 12
Idle
Job completed

## Slide 45: Johnson’s Rule Example
Time 0 3 10 20 28 33
Time 0 1 3 5 7 9 10 11 12 13 17 19 21 22 23 25 27 29 31 33 35
B
A
C
D
E
B
A
C
D
E
WC 1
WC 2
B
E
D
C
A
B
A
C
D
E
JOB | WORK CENTER 1 (DRILL PRESS) | WORK CENTER 2 (LATHE)
A | 5 | 2
B | 3 | 6
C | 8 | 4
D | 10 | 7
E | 7 | 12
Idle
Job completed

## Slide 46: Scheduling Services
Service systems differ from manufacturing
MANUFACTURING | SERVICES
Schedules machines and materials | Schedule staff
Inventories used to smooth demand | Seldom maintain inventories
Machine-intensive and demand may be smooth | Labor-intensive and demand may be variable
Scheduling may be bound by union contracts | Legal issues may constrain flexible scheduling
Few social or behavioral issues | Social and behavioral issues may be quite important

## Slide 47: Scheduling Services
Hospitals have complex scheduling systems to handle complex processes and material requirements
Banks use a cross-trained and flexible workforce and part-time workers
Retail stores use scheduling optimization systems that track sales, transactions, and customer traffic to create work schedules in less time and with improved customer satisfaction

## Slide 48: Scheduling Services
Airlines must meet complex FAA and union regulations and often use linear programming to develop optimal schedules
24/7 operations like police/fire departments, emergency hot lines, and mail order businesses use flexible workers and variable schedules, often created using computerized systems

## Slide 49: Scheduling Service Employees With Cyclical Scheduling
Objective is to meet staffing requirements with the minimum number of workers
Schedules need to be smooth and keep personnel happy
Many techniques exist from simple algorithms to complex linear programming solutions

## Slide 50: Cyclical Scheduling Example
Determine the staffing requirements
Identify two consecutive days with the lowest total requirements and assign these as days off
Make a new set of requirements subtracting the days worked by the first employee
Apply step 2 to the new row
Repeat steps 3 and 4 until all requirements have been met

## Slide 51: Cyclical Scheduling Example
 | M | T | W | T | F | S | S
Employee 1 | 5 | 5 | 6 | 5 | 4 | 3 | 3
Capacity (Employees) |  |  |  |  |  |  | 
Excess Capacity |  |  |  |  |  |  | 
DAY | M | T | W | T | F | S | S
Staff required | 5 | 5 | 6 | 5 | 4 | 3 | 3

## Slide 52: Cyclical Scheduling Example
 | M | T | W | T | F | S | S
Employee 1 | 5 | 5 | 6 | 5 | 4 | 3 | 3
Employee 2 | 4 | 4 | 5 | 4 | 3 | 3 | 3
Capacity (Employees) |  |  |  |  |  |  | 
Excess Capacity |  |  |  |  |  |  | 
DAY | M | T | W | T | F | S | S
Staff required | 5 | 5 | 6 | 5 | 4 | 3 | 3

## Slide 53: Cyclical Scheduling Example
 | M | T | W | T | F | S | S
Employee 1 | 5 | 5 | 6 | 5 | 4 | 3 | 3
Employee 2 | 4 | 4 | 5 | 4 | 3 | 3 | 3
Employee 3 | 3 | 3 | 4 | 3 | 2 | 3 | 3
Capacity (Employees) |  |  |  |  |  |  | 
Excess Capacity |  |  |  |  |  |  | 
DAY | M | T | W | T | F | S | S
Staff required | 5 | 5 | 6 | 5 | 4 | 3 | 3

## Slide 54: Cyclical Scheduling Example
 | M | T | W | T | F | S | S
Employee 1 | 5 | 5 | 6 | 5 | 4 | 3 | 3
Employee 2 | 4 | 4 | 5 | 4 | 3 | 3 | 3
Employee 3 | 3 | 3 | 4 | 3 | 2 | 3 | 3
Employee 4 | 2 | 2 | 3 | 2 | 2 | 3 | 2
Capacity (Employees) |  |  |  |  |  |  | 
Excess Capacity |  |  |  |  |  |  | 
DAY | M | T | W | T | F | S | S
Staff required | 5 | 5 | 6 | 5 | 4 | 3 | 3

## Slide 55: Cyclical Scheduling Example
 | M | T | W | T | F | S | S
Employee 1 | 5 | 5 | 6 | 5 | 4 | 3 | 3
Employee 2 | 4 | 4 | 5 | 4 | 3 | 3 | 3
Employee 3 | 3 | 3 | 4 | 3 | 2 | 3 | 3
Employee 4 | 2 | 2 | 3 | 2 | 2 | 3 | 2
Employee 5 | 1 | 1 | 2 | 2 | 2 | 2 | 1
Capacity (Employees) |  |  |  |  |  |  | 
Excess Capacity |  |  |  |  |  |  | 
DAY | M | T | W | T | F | S | S
Staff required | 5 | 5 | 6 | 5 | 4 | 3 | 3

## Slide 56: Cyclical Scheduling Example
 | M | T | W | T | F | S | S
Employee 1 | 5 | 5 | 6 | 5 | 4 | 3 | 3
Employee 2 | 4 | 4 | 5 | 4 | 3 | 3 | 3
Employee 3 | 3 | 3 | 4 | 3 | 2 | 3 | 3
Employee 4 | 2 | 2 | 3 | 2 | 2 | 3 | 2
Employee 5 | 1 | 1 | 2 | 2 | 2 | 2 | 1
Employee 6 | 1 | 1 | 1 | 1 | 1 | 1 | 0
Capacity (Employees) |  |  |  |  |  |  | 
Excess Capacity |  |  |  |  |  |  | 
DAY | M | T | W | T | F | S | S
Staff required | 5 | 5 | 6 | 5 | 4 | 3 | 3

## Slide 57: Cyclical Scheduling Example
 | M | T | W | T | F | S | S
Employee 1 | 5 | 5 | 6 | 5 | 4 | 3 | 3
Employee 2 | 4 | 4 | 5 | 4 | 3 | 3 | 3
Employee 3 | 3 | 3 | 4 | 3 | 2 | 3 | 3
Employee 4 | 2 | 2 | 3 | 2 | 2 | 3 | 2
Employee 5 | 1 | 1 | 2 | 2 | 2 | 2 | 1
Employee 6 | 1 | 1 | 1 | 1 | 1 | 1 | 0
Employee 7 |  |  |  |  |  | 1 | 
Capacity (Employees) | 5 | 5 | 6 | 5 | 4 | 3 | 3
Excess Capacity | 0 | 0 | 0 | 0 | 0 | 1 | 0
DAY | M | T | W | T | F | S | S
Staff required | 5 | 5 | 6 | 5 | 4 | 3 | 3