## Slide 1
Process Strategy
PowerPoint presentation to accompany
Heizer, Render, Munson
Operations Management, Twelfth Edition, Global Edition
Principles of Operations Management, Tenth Edition, Global Edition
PowerPoint slides by Jeff Heyl
7

## Slide 2: Process Flow Diagram
THE ASSEMBLY LINE
TESTING
28 tests
Oil tank work cell
Shocks and forks
Handlebars
Fender work cell
Air cleaners
Fluids and mufflers
Fuel tank work cell
Wheel work cell
Roller testing
Incoming parts
Arrive on a JIT schedule from a 10-station work cell in Milwaukee
Engines and transmissions
Frame tube bending
Frame-building work cells
Frame machining
Hot-paint
frame painting
Crating

## Slide 3: Learning Objectives
When you complete this chapter you should be able to:
7.1 Describe four process strategies
7.2 Compute crossover points for different processes
7.3 Use the tools of process analysis
7.4 Describe customer interaction in service processes
7.5 Identify recent advances in production technology

## Slide 4: Process Strategy
The objective is to create a process to produce offerings that meet customer requirements within cost and other managerial constraints

## Slide 5: Process Strategies
How to produce a product or provide a service that
  Meets or exceeds customer requirements
  Meets cost and managerial goals
Has long term effects on
  Efficiency and production flexibility
  Costs and quality

## Slide 6: Process, Volume, and Variety
Process Focus
projects, job shops (machine, print, hospitals, restaurants)
Arnold Palmer Hospital
Repetitive
(autos, motorcycles, home appliances)
Harley-Davidson
Product Focus
(commercial baked goods, steel, glass, beer)
Frito-Lay
High Variety
one or few units per run,
(allows customization)
Changes in Modules
modest runs, standardized modules
Changes in Attributes (such as grade, quality, size, thickness, etc.)
long runs only
Mass Customization
(difficult to achieve, but huge rewards)
Dell Computer
Poor Strategy (Both fixed and variable costs are high)
Low Volume
Repetitive Process
High Volume
Volume
Figure 7.1
Variety (flexibility)

## Slide 7: Process Strategies
Four basic strategies
Process focus
Repetitive focus
Product focus
Mass customization
Within these basic strategies there are many ways they may be implemented

## Slide 8: Process Focus
Facilities are organized around specific activities or processes
General purpose equipment and skilled personnel
High degree of product flexibility
Typically high costs and low equipment utilization
Product flows may vary considerably making planning and scheduling a challenge

## Slide 9: Process Focus
Many inputs
(surgeries, sick patients, baby deliveries, emergencies)
Many different outputs (uniquely treated patients)
Many departments and many routings
Figure 7.2(a)
(low-volume, high-variety, intermittent processes)
Arnold Palmer Hospital

## Slide 10: Repetitive Focus
Facilities often organized as assembly lines
Characterized by modules with parts and assemblies made previously
Modules may be combined for many output options
Less flexibility than process-focused facilities but more efficient

## Slide 11: Repetitive Focus
Raw materials and module inputs
Modules combined for many
Output options
(many combinations of motorcycles)
Few modules
(multiple engine models, wheel modules)
Figure 7.2(b)
(modular)
Harley Davidson

## Slide 12: Product Focus
Facilities are organized by product
High volume but low variety of products
Long, continuous production runs enable efficient processes
Typically high fixed cost but low variable cost
Generally less skilled labor

## Slide 13: Product Focus
Few inputs
(corn, potatoes, water, seasoning)
Output variations in size, shape, and packaging
(3-oz, 5-oz, 24-oz package labeled for each material)
Figure 7.2(c)
(high-volume, low-variety, continuous process)
Frito-Lay

## Slide 14: Mass Customization
The rapid, low-cost production of goods and service to satisfy increasingly unique customer desires
Combines the flexibility of a process focus with the efficiency of a product focus

## Slide 15: Mass Customization
Figure 7.2(b)
(high-volume, high-variety)
Dell Computer
Many parts and component inputs
Many output versions
(custom PCs and notebooks)
(chips, hard drives, software, cases)
Many modules

## Slide 16: Mass Customization
TABLE 7.1 | Mass Customization Provides More Choices Than Ever |  | 
 |  | NUMBER OF CHOICES | 
ITEM |  | 1970s | 21ST CENTURY
Vehicle styles |  | 18 | 1,212
Bicycle types |  | 8 | 211,000
iPhone mobile game apps |  | 0 | 1,200,000
Web sites |  | 0 | 634,000,000
Movie releases per year |  | 267 | 1551
New book titles |  | 40,530 | 300,000+
Houston TV channels |  | 5 | 185
Breakfast cereals |  | 160 | 340
Items (SKUs) in supermarkets |  | 14,000 | 150,000
High-definition TVs |  | 0 | 102

## Slide 17: Mass Customization
Imaginative product design
Flexible process design
Tightly controlled inventory management
Tight schedules
Responsive partners in the supply-chain

## Slide 18: Comparison of Processes
TABLE 7.2 | Comparison of the Characteristics of Four Types of Processes |  |  | 
PROCESS FOCUS (LOW-VOLUME, HIGH-VARIETY ARNOLD PALMER HOSPITAL) |  | REPETITIVE FOCUS (MODULAR HARLEY-DAVIDSON) | PRODUCT FOCUS (HIGH-VOLUME, LOW-VARIETY FRITO-LAY) | MASS CUSTOMIZATION (HIGH-VOLUME, HIGH-VARIETY DELL COMPUTER)
Small quantity and large variety of products |  | Long runs, a standardized product from modules | Large quantity and small variety of products | Large quantity and large variety of products
Broadly skilled operators |  | Moderately trained employees | Less broadly skilled operators | Flexible operators

## Slide 19: Comparison of Processes
TABLE 7.2 | Comparison of the Characteristics of Four Types of Processes |  |  | 
PROCESS FOCUS (LOW-VOLUME, HIGH-VARIETY ARNOLD PALMER HOSPITAL) |  | REPETITIVE FOCUS (MODULAR HARLEY-DAVIDSON) | PRODUCT FOCUS (HIGH-VOLUME, LOW-VARIETY FRITO-LAY) | MASS CUSTOMIZATION (HIGH-VOLUME, HIGH-VARIETY DELL COMPUTER)
Instructions for each job |  | Few changes in the instructions | Standardized job instructions | Custom orders requiring many job instructions
High inventory |  | Low inventory | Low inventory | Low inventory relative to the value of the product

## Slide 20: Comparison of Processes
TABLE 7.2 | Comparison of the Characteristics of Four Types of Processes |  |  | 
PROCESS FOCUS (LOW-VOLUME, HIGH-VARIETY ARNOLD PALMER HOSPITAL) |  | REPETITIVE FOCUS (MODULAR HARLEY-DAVIDSON) | PRODUCT FOCUS (HIGH-VOLUME, LOW-VARIETY FRITO-LAY) | MASS CUSTOMIZATION (HIGH-VOLUME, HIGH-VARIETY DELL COMPUTER)
Finished goods are made to order and not stored |  | Finished goods are made to frequent forecasts | Finished goods are made to a forecast and stored | Finished goods are build-to-order (BTO)
Scheduling is complex |  | Scheduling is routine | Scheduling is routine | Sophisticated scheduling accommodates custom orders

## Slide 21: Comparison of Processes
TABLE 7.2 | Comparison of the Characteristics of Four Types of Processes |  |  | 
PROCESS FOCUS (LOW-VOLUME, HIGH-VARIETY ARNOLD PALMER HOSPITAL) |  | REPETITIVE FOCUS (MODULAR HARLEY-DAVIDSON) | PRODUCT FOCUS (HIGH-VOLUME, LOW-VARIETY FRITO-LAY) | MASS CUSTOMIZATION (HIGH-VOLUME, HIGH-VARIETY DELL COMPUTER)
Fixed costs are low and variable costs high |  | Fixed costs are dependent on flexibility of the facility | Fixed costs are high and variable costs low | Fixed costs tend to be high and variable costs low

## Slide 22: Crossover Chart Example
Evaluate three different accounting software products
Calculate crossover points between software A and B and between software B and C
 | TOTAL FIXED COST | DOLLARS REQUIRED PER ACCOUNTING REPORT
Software A | $200,000 | $60
Software B | $300,000 | $25
Software C | $400,000 | $10

## Slide 23: Crossover Chart Example
Software A is most economical from 0 to 2,857 reports
Software B is most economical from 2,857 to 6,666 reports

## Slide 24: Crossover Charts
Fixed costs
Variable costs
$
High volume, low variety
Process C
Fixed costs
Variable costs
$
Repetitive
Process B
Fixed costs
Variable costs
$
Low volume, high variety
Process A
Fixed cost Process A
Fixed cost Process B
Fixed cost Process C
Total process A costs
Total process B costs
Total process C costs
V1
(2,857)
V2
(6,666)
400,000
300,000
200,000
Volume
$
Figure 7.3

## Slide 25: Focused Processes
Focus brings efficiency
Focus on depth of product line rather than breadth
Focus can be
  Customers
  Products
  Service
  Technology

## Slide 26: Selection of Equipment
Decisions can be complex as alternate methods may be available
Important factors may be
  Cost
  Cash flow
  Market stability
  Quality
  Capacity
  Flexibility

## Slide 27: Flexibility
Flexibility is the ability to respond with little penalty in time, cost, or customer value
May be a competitive advantage
May be difficult and expensive
Without it, change may mean starting over

## Slide 28: Process Analysis and Design
Is the process designed to achieve a competitive advantage?
Does the process eliminate steps that do not add value?
Does the process maximize customer value?
Will the process win orders?

## Slide 29: Process Analysis and Design
Flowchart
  Shows the movement of materials
  Harley-Davidson flowchart
Time-Function Mapping
  Shows flows and time frame

## Slide 30: "Baseline" Time-Function Map
Customer
Sales
Production control
Plant A
Warehouse
Plant B
Transport
12 days
13 days
1 day
4 days
1 day
10 days
1 day
9 day
1 day
52 days
Figure 7.4(a)
Move
Receive product
Product
Product
Extrude
Wait
WIP
Product
Move
Wait
WIP
WIP
Print
Wait
Order
WIP
Order product
Process order
Wait
Order

## Slide 31: "Target" Time-Function Map
Customer
Sales
Production control
Plant
Warehouse
Transport
1 day
2 days
1 day
1 day
1 day
6 days
Figure 7.4(b)
Move
Receive product
Product
Product
Extrude
Wait
Print
Order
WIP
Product
Order product
Process order
Wait
Order

## Slide 32: Process Chart
Figure 7.5

## Slide 33: Process Analysis and Design
Value-Stream Mapping (VSM)
  Where value is added in the entire production process, including the supply chain
  Extends from the customer back to the suppliers

## Slide 34: Value-Stream Mapping
Begin with symbols for customer, supplier, and production to ensure the big picture
Enter customer order requirements
Calculate the daily production requirements
Enter the outbound shipping requirements and delivery frequency
Determine inbound shipping method and delivery frequency

## Slide 35: Value-Stream Mapping
Add the process steps (i.e., machine, assemble) in sequence, left to right
Add communication methods, add their frequency, and show the direction with arrows
Add inventory quantities between every step of the entire flow
Determine total working time (value-added time) and delay (non-value-added time)
I

## Slide 36: Value-Stream Mapping
Figure 7.6

## Slide 37: Service Blueprinting
Focuses on the customer and provider interaction
Defines three levels of interaction
Each level has different management issues
Identifies potential failure points

## Slide 38: Service Blueprint
Personal Greeting
Service Diagnosis
Perform Service
Friendly Close
Level
#3
Level
#1
Level
#2
Figure 7.7
No
Notify customer and recommend an alternative provider.
(7 min)
Customer arrives for service.
(3 min)
Warm greeting and obtain service request.
(10 sec)
F
Direct customer to waiting room.
F
Notify customer the car is ready.
(3 min)
Customer departs
Customer pays bill.
(4 min)
F
F
Perform required work.
(varies)
Prepare invoice.
(3 min)
F
F
Yes
F
Yes
F
Standard request.
(3 min)
Determine specifics.
(5 min)
No
Can service be done and does customer approve?
(5 min)

## Slide 39: Special Considerations for Service Process Design
Some interaction with customer is necessary, but this often affects performance adversely
The better these interactions are accommodated in the process design, the more efficient and effective the process
Find the right combination of cost and customer interaction

## Slide 40: Service Process Matrix
Service Factory
Service Shop
Degree of Customization
Low
High
Degree of Labor
Low
High
Mass Service
Professional Service
Commercial banking
Private banking
General-
purpose law firms
Law clinics
Specialized hospitals
Hospitals
Full-service stockbroker
Limited-service stockbroker
Retailing
Boutiques
Warehouse and catalog stores
Fast-food restaurants
Fine-dining restaurants
Airlines
No-frills airlines
Figure 7.8
Digitized orthodontics
Traditional orthodontics

## Slide 41: Service Process Matrix
Labor involvement is high
Focus on human resources
Selection and training highly important
Personalized services
Mass Service and Professional Service
Service Factory
Service Shop
Degree of Customization
Low
High
Degree of Labor
Low
High
Mass Service
Professional Service
Commercial banking
Private banking
General-
purpose law firms
Law clinics
Specialized hospitals
Hospitals
Full-service stockbroker
Limited-service stockbroker
Retailing
Boutiques
Warehouse and catalog stores
Fast-food restaurants
Fine-dining restaurants
Airlines
No-frills airlines
Digital orthodontics
Traditional orthodontics

## Slide 42: Service Process Matrix
Service Factory and Service Shop
Automation of standardized services
Restricted offerings
Low labor intensity responds well to process technology and scheduling
Tight control required to maintain standards
Service Factory
Service Shop
Degree of Customization
Low
High
Degree of Labor
Low
High
Mass Service
Professional Service
Commercial banking
Private banking
General-
purpose law firms
Law clinics
Specialized hospitals
Hospitals
Full-service stockbroker
Limited-service stockbroker
Retailing
Boutiques
Warehouse and catalog stores
Fast-food restaurants
Fine-dining restaurants
Airlines
No-frills airlines
Digital orthodontics
Traditional orthodontics

## Slide 43: Improving Service Productivity
TABLE 7.3 | Techniques for Improving Service Productivity |  | 
STRATEGY |  | TECHNIQUE | EXAMPLE
Separation |  | Structuring service so customers must go where the service is offered | Bank customers go to a manager to open a new account, to loan officers for loans, and to tellers for deposits
Self-service |  | Self-service so customers examine, compare, and evaluate at their own pace | Supermarkets and department stores Internet ordering
Postponement |  | Customizing at delivery | Customizing vans at delivery rather than at production
Focus |  | Restricting the offerings | Limited-menu restaurant

## Slide 44: Improving Service Productivity
TABLE 7.3 | Techniques for Improving Service Productivity |  | 
STRATEGY |  | TECHNIQUE | EXAMPLE
Modules |  | Modular selection of service Modular production | Investment and insurance selection Prepackaged food modules in restaurants
Automation |  | Separating services that may lend themselves to some type of automation | Automatic teller machines
Scheduling |  | Precise personnel scheduling | Scheduling ticket counter personnel at 15-minute intervals at airlines
Training |  | Clarifying the service options Explaining how to avoid problems | Investment counselor, funeral directors After-sale maintenance personnel

## Slide 45: Production Technology
Machine technology
Automatic identification systems (AISs)
Process control
Vision systems
Robots
Automated storage and retrieval systems (ASRSs)
Automated guided vehicles (AGVs)
Flexible manufacturing systems (FMSs)
Computer-integrated manufacturing (CIM)

## Slide 46: Machine Technology
Increased precision, productivity, and flexibility
Reduced environmental impact
Additive manufacturing produces products by adding material, not removing it
Supports innovative product design, minimal custom tooling required, minimal assembly time, low inventory, and reduced time to market
Computer numerical
control (CNC)

## Slide 47: Automatic Identification Systems (AISs) and RFID
Improved data acquisition
Reduced data entry errors
Increased speed
Increased scope of process automation
Bar codes and RFID

## Slide 48: Process Control
Real-time monitoring and control of processes
  Sensors collect data
  Devices read data on periodic basis
  Measurements translated into digital signals then sent to a computer
  Computer programs analyze the data
  Resulting output may take numerous forms

## Slide 49: Vision Systems
Particular aid to inspection
Consistently accurate
Never bored
Modest cost
Superior to individuals performing the same tasks

## Slide 50: Robots
Perform monotonous or dangerous tasks
Perform tasks requiring significant strength or endurance
Generally enhanced consistency and accuracy

## Slide 51: Automated Storage and Retrieval Systems (ASRSs)
Automated placement and withdrawal of parts and products
Reduced errors and labor
Particularly useful in inventory and test areas of manufacturing firms

## Slide 52: Automated Guided Vehicle (AGVs)
Electronically guided and controlled carts
Used for movement of products and/or individuals

## Slide 53: Flexible Manufacturing Systems (FMSs)
Computer controls both the workstation and the material handling equipment
Enhance flexibility and reduced waste
Can economically produce low volume but high variety
Reduced changeover time and increased utilization
Stringent communication requirement between components

## Slide 54: Computer-Integrated Manufacturing (CIM)
Extend flexible manufacturing
  Backward to engineering and inventory control
  Forward into warehousing and shipping
  Can also include financial and customer service areas
  Reducing the distinction between low-volume/high-variety, and high-volume/low-variety production

## Slide 55: Computer-Integrated Manufacturing (CIM)
Figure 7.9

## Slide 56: Technology in Services
TABLE 7.4 | Examples of Technology's Impact on Services | 
SERVICE INDUSTRY |  | EXAMPLE
Financial Services |  | Debit cards, electronic funds transfer, ATMs, Internet stock trading, online banking via cell phone
Education |  | Online newspapers and journals, interactive assignments via WebCT, Blackboard, and smartphones
Utilities and government |  | Automated one-person garbage trucks, optical mail scanners, flood-warning systems, meters that allow homeowners to control energy usage and costs
Restaurants and foods |  | Wireless orders from waiters to kitchen, robot butchering, transponders on cars that track sales at drive-throughs
Communications |  | Interactive TV, e-books via Kindle

## Slide 57: Technology in Services
TABLE 7.4 | Examples of Technology’s Impact on Services | 
SERVICE INDUSTRY |  | EXAMPLE
Hotels |  | Electronic check-in/check-out, electronic key/lock systems, mobile Web bookings
Wholesale/retail trade |  | Point-of-sale (POS) terminals, e-commerce, electronic communication between store and supplier, bar-coded data, RFID
Transportation |  | Automatic toll booths, satellite-directed navigation systems, Wi-Fi in automobiles
Health care |  | Online patient-monitoring systems, online medical information systems, robotic surgery
Airlines |  | Ticketless travel, scheduling, Internet purchases, boarding passes downloaded as two-dimensional bar codes on smart phones